## Slide 1: Domestic Power

## Slide 2: The basic unit of energy
… is the joule (J). It is a very small unit, so when we are talking about a lot of energy, we use kilojoules (kJ).
Remember your metric conversions…
1000 J = 1 kJ (kilo = 1000)

## Slide 3: Power
Power (P) is the rate at which energy is used.
  When determining the amount of energy (usually in J or kJ) you must also include a time component.
Power x Time = Energy (P x t = E)
  This can be rearranged to determine power as well
P = E/t (Power = Energy /time)

## Slide 4: Efficiency
The unit for power is the Watt (W)
  1 W = 1 J/sec (1 watt = 1 joule per second)
Therefore a 100 W light bulb uses
100 J/sec of electrical energy.
Efficiency (%) = Energy output x 100
Energy input
If it is 20% efficient (typical for an average light bulb) then the bulb converts 20% of the electrical energy into light, and 80% is lost as waste heat.

## Slide 5: Solution
How much energy in J does a 75 W light bulb use when it is turned on for 25 minutes?
E = 75 J 60 sec 25 min
sec min
110 000 J
(or 110 kJ)

## Slide 6: If the wattage is not given
Some of the information about the current can usually be found.
To find the power (in watts) of any electrical appliance, use the equation P = V x I
  P = power, V = voltage, I is current in amperes (A).
Australian household voltage is 250 V (Some air conditioners, electric stoves and
dryers are 220 V).

## Slide 7: Kilowatt Hour
The Kilowatt Hour (kWh) is not a unit of power but a unit of energy (because it has a time component).
  Notice that a kilowatt is a unit of power and hour is a unit of time. Therefore, E = P x t.
A kilowatt hour is equal to 1 kW (or 1000 W) delivered continuously for one hour (3600 s).
1 kWh = 1000 J/s x 3600 s = 3 600 000 J or 3600 kJ

## Slide 8: Problem 1
Dr. Smith’s power bill shows that his home used 1355 kWh over a 30 day period.
  1 kwh = 3600 kJ
  Find the energy used (in kJ) for the 30-day period.
  Find the energy used in J/day.
  At the rate of $0.075 per kWh, what is Dr. Smith’s power bill (without tax)?

## Slide 9: 1a
1355 kWh in 30 days
Find the energy used (in kJ) for the 30 day
period.
1355 kWh 3600 kJ 4.88 x 106 kJ
1 kWh

## Slide 10: 1b
  Find the energy used in J/day.
  Start with previous calculation
  4.88 x 106 kJ 1000 J 1 month 1.63 x 108 J/day
  Month 1 kJ 30 days

## Slide 11: 1c
  At the rate of $0.075 per kWh find Dr. Smith’s power
  bill (without tax).
  1355 kwh $.075 $101.63
  1 kwh

## Slide 12: Problem 2
A current through a toaster (110 V) is 8.00 A. Remember, P = V x I
  What is the power (in Watts) of the toaster?
  How much energy (in J) will the toaster use in
  5 minutes of operation?

## Slide 13: 2a
  A current through a toaster (110 V) is 8.00 A.
  What is the power (in watts) of the toaster?
P = V x I
where V = voltage and I = amperes
P = 110V x 8.00 A = 880 W

## Slide 14: 2b
How much energy (in J) will the toaster use in 5 minutes of operation?
P = E/t so E = P x t
  (1 Watt = 1 Joule per second)
E = 880 W (1 J/sec) 60 sec 5 min 264,000 J
1 W min
= 2.64 x 105 J

## Slide 15: Problem 3
A 100 W light bulb is 20% efficient. That means 20% of the energy used is converted to light, while 80% of the energy used is lost as heat.
  How much energy does it use in 12 hours of operation?
  How much energy does the bulb convert into light over the 12 hour period?
  How much energy does the bulb convert into heat over the 12 hour period?
  Convert the total energy use into kWh

## Slide 16: 3a
A 100 W light bulb is 20% efficient.
How much energy does it use in 12 hours of
operation?
E = P x t
E = 100 W (1 J/sec) 60 sec 60 min 12 hrs
1 watt min 1 hr
= 4,320,000 J
= 4,320 kJ

## Slide 17: 3b
  How much energy does the bulb convert into light over the 12 hour period?
  E = 4.32 x 106 J x 20/100 (efficiency)
  = 864 000 J = 8.64 x 105 J

## Slide 18: 3c
How much energy does the bulb convert into
heat over the 12 hour period?
E = 4.32 x 106 J x 80/100 (heat)
= 3 456 000 J
= 3.46 x 106 J of heat energy

## Slide 19: 3d
Convert the total energy use into kWh.
The energy calculated in 3a) was 4 320 000 J
1 kwh = 3 600 000 J
4 320 000 = 1.2 kWh
3 600 000

## Slide 20: Problem 4
An electric clothes dryer has a power rating of 4000W. A family does five loads of laundry each week for 4 weeks. If each load takes one hour.
  Find the energy used in both J and kWh
  If the cost of electricity is $0.075 per kWh, find the cost of operating the dryer for 4 weeks.

## Slide 21: 4a
Find the energy used in both J and kWh
5 loads x 4 weeks x 1 hr = 20 hrs
week load
E = P x t
E = 4000 W x (1 J/sec) x 60 sec x 60 min x 20 hrs = 2.88 x 108 J 1 watt min hr
2.88 x 105 kJ x 1 kWh = 80 kWh
3600 kJ

## Slide 22: 4b
If the cost of electricity is $0.075 per kWh, find the cost of operating the dryer for 4 weeks.
80 kWh x $0.075 per kWh = $6.00

## Slide 23: Problem 5
Dr. Smith’s natural gas bill states that his household used 108 MJ of energy over a 30 day period.
  Convert 108 MJ to kWh.
  His charge for the energy was $88.78. Find the cost of this natural gas in $AUD per kWh.
  Using the information about electricity costs in the problems above, which form of energy (electricity or natural gas) is more expensive? How many times more expensive is it?

## Slide 24: 5a
Convert 108 MJ to kWh
108 MJ = 108 000 000 = 108 = 30 kWhr
3 600 000 3.6 1
= 30.0 kWh

## Slide 25: 5b
His charge for the energy was $88.78. Find
the cost of this natural gas in $AUD kWh.
$88.78 / 30 kWh = $2.96 per kWh

## Slide 26: 5c
Which form of energy (electricity or natural gas) is more expensive? How many times more expensive is it?
electricity: $0.075 natural gas: $2.96
Ratio = 2.96 = 39.52
0.075
Natural gas is about 39.5 times more expensive